## Slide 1
THREE-WAY MODEL COMPARISON
Stanford vs ECGFounder paper vs This repo
The 2019 baseline, the 2025 foundation model, and what we deploy on top of it
Stanford = external baseline ECGFounder = our base model Repo = ECGFounder + project layers

## Slide 2
NOT THREE RIVALS — A BASELINE, A BASE MODEL, AND OUR BUILD
How the three relate
Stanford 1D-ResNet
Nature Medicine 2019
External, independent baseline — a different paradigm (seq-to-seq, trained per dataset).
BASELINE
ECGFounder (Li 2025)
Pretrained foundation model
10.8M ECGs, 150-label space, single-lead via lead augmentation.
OUR BASE MODEL
This repo
ECGFounder + project layers
7-label scope, fuzzy probe, DualHead, FP gates, reporting.
WHAT WE DEPLOY
Two threads tie them together
1. ECGFounder adopts Hannun's 3-cardiologist committee evaluation design (it cites the 2019 paper).
2. Hannun explicitly warns that running the model across long recordings yields “non-trivial false-positive diagnoses” — exactly the problem our motion/SQI gates and per-window reporting solve.
3. ECGFounder's single-lead lead-augmentation is re-implemented in this repo as the PTB-XL fuzzy-angle dataset.

## Slide 3
DESIGN AND DATA
Side-by-side (1 of 2)
Dimension | Stanford 2019 | ECGFounder 2025 (paper) | This repo (deployed)
Role | External baseline | Our base model (as published) | Founder + project layers
Paradigm | Trained from scratch | Pretrained foundation | Foundation + probe / gates
Pretraining data | 91K rec / 53.5K patients (Zio) | 10.8M ECGs / 1.8M subjects (HEEDB) | inherits Founder pretraining
Leads / input | 1-lead Zio, 200 Hz, 30 s-days | 12-lead 10 s (+1-lead lead-aug) | 1-lead 500 Hz, 10 s (1x5000)
Architecture | 34-layer 1D ResNet | Net1D / RegNet + attention | same Net1D (~30.8M params)
Output | seq-to-seq softmax / 1.28 s | per-record sigmoid, 150 heads | per-10 s window -> merged events
Label space | 12 exclusive rhythms | 150 multi-label diagnoses | 7-label scope (global hard rule)

## Slide 4
ADAPTATION, EVALUATION, RESULTS
Side-by-side (2 of 2)
Dimension | Stanford 2019 | ECGFounder 2025 (paper) | This repo (deployed)
Adaptation | retrain per dataset | linear probe / full fine-tune | scope linear probe + DualHead
Evaluation | 3-card committee + 6 indiv | same committee (cites Hannun) | PTB-XL 1-8/9/10; fzark/MIT-BIH/MOVE
Headline numbers | AUC 0.97, F1 .837 > .780 (in-dist) | committee AUROC .968; CODE .981 | probe fold-10 ROC .970; AF ~.95 zero-shot
Single-lead AF | cinc17 ckpt has an 'A' class | external 1-lead AF AUROC 0.957 | zero-shot ~0.95 + motion gate
Long-recording FP | acknowledged, unsolved | cloud-side, not in-model | motion + SQI gates + windowing
Cross-DB labels | none (retrain / hand-map) | fixed 150-space, centralized | label_config + GLOBAL_LABEL_MAP (enforced)
Openness | code open; data proprietary | code + model + data open | built on the open Founder release

## Slide 5
THE PROJECT LAYERS ON TOP OF THE FOUNDATION MODEL
What this repo adds to ECGFounder
7-label detection scope
Global hard rule: Normal, Bradycardia, AFib, Sinus Tachycardia, SV Run, V Run, Pause. Everything else is inert.
Fuzzy-angle linear probe
Re-implements the paper's lead augmentation on PTB-XL (45/60/75/90 deg). Frozen backbone, 6 readout rows; fold-10 macro ROC 0.970.
DualHead routing
Runtime router over base + fine-tuned checkpoints, per-head selection (scope route = the 6 probe heads).
Split FP suppression
Independent, separately-trainable motion (accelerometer) and SQI (ECG-intrinsic) gates; per-device profiles.
Per-recording reporting
report_recording.py windows long strips into events + burden % + explicit raw -> after-FP accounting.
PTB-XL 1-8/9/10 splits
Enforced patient-stratified train/val/test (import-time integrity check, 0 leakage).

## Slide 6
WHERE THE THREE ACTUALLY DIFFER ON NUMBERS
The metrics that matter
AFib — the strong case
Founder 1-lead external: AUROC 0.957
Repo zero-shot (fzark/MIT-BIH): ~0.95
Motion gate cuts MOVE false AFib ~90%
Stanford: only cinc17 ckpt has an 'A' class
VT — the single-lead gap
Founder 12-lead: 0.903 (committee) / 0.987 (PTB-XL)
Repo measured 1-lead: ~0.36 (worse than chance)
12-lead VT strength does NOT survive single-lead
This is why the FP gates exist
Overall / Normal
Founder 1-lead NSR external: AUROC 0.975
Repo scope probe fold-10 macro ROC: 0.970
Non-target head drift: 0.00e+00
Stanford in-dist: AUC 0.97 (different task)
In-distribution fit (Stanford) vs external transfer (Founder/repo) measure different things — read the caveats slide.

## Slide 7
VERDICT
When each matters
Stanford
Per-segment rhythm timeline (1.28 s) on a continuous strip
High specificity when trained on your distribution
Use as an independent, in-distribution baseline
Narrow: few exclusive classes, no transfer
ECGFounder paper
Broad 150-label diagnosis with transfer
Single-lead capable via lead augmentation
Cloud-side analysis of wearable uploads
The right backbone to build on
This repo
Founder focused to a clinical 7-label scope
FP gates + per-window reporting for long strips
Centralized, enforced cross-dataset label map
What you actually deploy on fzark / MOVE
Complementary, not competing — and the repo is the foundation model made deployable.

## Slide 8
READ BEFORE QUOTING ANY NUMBER
Caveats
Different settings
Stanford numbers are in-distribution (trained on MIT-BIH/Zio); Founder/repo numbers are external transfer. They measure fit vs generalization.
Different label spaces / granularity
12 exclusive rhythms @1.28 s vs 150 multi-label @record vs 7-label scope @10 s window. Per-class F1 is not directly comparable.
Single-lead VT is weak
The Founder paper's strong VT is 12-lead; at single lead it collapses (~0.36 here). Treat VT detections with the FP gate.
No ground truth on MOVE
MOVE comparisons are false-positive / reporting-format behavior, not validated accuracy.
Executive Summary errors
That ChatGPT digest says 14 classes (it's 12) and 1 label/second (it's 1 / 1.28 s), and never covers ECGFounder.